Seminar Parallel- und Realzeitsysteme WS 2006/2007 Thema der Arbeit
Thema der Arbeit
Userspace Linux on the BeagleBone
Guillaume Quéré
WS 20011/2012

---
Folientitel
BeagleBone
BeagleBone
  - AM3359
    - 720MHz
  - 256MB DDR2
  - USB, ethernet
  - PWM, Timers, LCD
  - UART, I²C, SPI, CAN
  - ~1W idle
  - 40 g, 12*5 cm^2
  - ~70 pins
          (picture credit : BB SRM)

---
Intro

---
Virtual filesystem
- Sysfs interface
  - Virtual filesystem
  - /sys/class ...
- Immediate alternatives :
  - Direct register access
  - PRUSS : Programmable Real-Time
    (picture credit: Uncle Joe from beagle list)

---
Realisation : D/A conversion
- Thermistor
- Steinhart and Hart's Law
- Implications
- Overall precision

---
GPIO : Communication
- Usual Applications
  - I²C, SPI … need voltage converter !
- HD44780 Controller
  - Parallel device
  - Usually, 2 rows of characters
- Timings for the HD44780
  - Commands vs Data

---
PWM
- Usual applications
  - IR, heating systems, dimmers, servomotors ...
- Enabling the PWM on BeagleBone :
  - Mmap system clock registers
  - Enable sysclock
  - Set correct MUX
  - Set duty, frequency, run

---
Interrupts
- Make a GPIO pin trigger an interrupt
  - Export pin
  - Set edge
  - Reset event set
  - Check for event poll(2)
  - Reset event set
  - …
- IR program :
  - Add timestamps
    - gettimeofday();

---
Video over http (with overlay)
- Usual way
  - V4l (Video for Linux) + C API for images (SDL ...)
- Here :
  - 2 instances of mjpeg-streamer
  - + ImageMagick conversion in the middle
  - = overlay apply
- Immediate drawbacks :
  - 2 fps
  - 15% CPU consumption
- Alternative : YUYV !

---
Database operations
- Usually, MySQL
- Here, SQLite
  - Very different architecture
  - Lightweight
  - Simple API
- Database C API functions :
  - sqlite3_open / sqlite3_close	// open / close
  - sqlite3_prepare	// prepare AND execute !
  - sqlite3_step	// get 1 line
  - sqlite3_exec	// execute

---
CGI Scripts

---
Conclusion